## Slide 1: PAPER ID: 282 HammerFilter: Robust Protection and Low Hardware Overhead Method for RowHammer
Kwangrae Kim
Department of EE
Hanyang University
Junsu Kim
Department of EE
Hanyang University
Jeonghyun Woo
Department of ECE
University of Illinois at Urbana-Champaign
Ki-Seok Chung
Department of EE
Hanyang University

## Slide 2
Background
Existing Solutions
Motivation&Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 3
Background
Existing Solutions
Motivation&Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 4
What is RowHammer?
Repeatedly access to a DRAM row (aggressor row) causes bit-flip in nearby rows (victim row)
  RowHammer
Row Decoder
Sense Amplifier
1
0
1
1
0
1
1
DRAM cell
1
1
0
0
1
1
1
Victim row
Victim row
Aggressor row
Access
DRAM Bank

## Slide 5
Why is RowHammer crucial to solve?
RowHammer can be used to make malicious application
  -> Security problem
  Ex) Gains kernel privileges on x86-64 Linux [Mark+, 2015]
As DRAM process technology scales down, RowHammer is getting worse
  RowHammer threshold (RH threshold) gets low
    Multiple aggressor rows can be attacked
    -> Get complicated
New attack patterns have been being introduced
  Ex) Double-sided attack, Half-Double attack

## Slide 6
RowHammer Attack Scenarios
Double-sided attack
  Makes the victim row between two aggressor rows more vulnerable to RowHammer attacks
Attack using multiple aggressor rows
  Complicate RowHamer attack can be made
VICTIM ROW
AGGRESSOR ROW
VICTIM ROW
AGGRESSOR ROW
VICTIM ROW
VICTIM ROW
AGGRESSOR ROW
VICTIM ROW
AGGRESSOR ROW
VICTIM ROW
VICTIM ROW
AGGRESSOR ROW

## Slide 7
Background
Existing Solutions
Motivation&Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 8
Hardware-based Protection Methods
Probabilistic methods:
  Perform additional refreshes with a certain probability
  Can be implemented with simple hardware circuit
  Have low protection performance
Counter-based methods:
  Keep track of every aggressor rows using counters
  Guarantee protection
  Suffer from considerate area overhead or extreme additional refreshes (related with performance overhead) or even both

## Slide 9
Previous Probabilistic Methods
They still cannot prevent well in the complicate attack
  PARA [Kim+, ISCA’14], MRLoc [You+, DAC’19], and PRoHIT [Son, DAC’17]
Chart: Aggressor Rows #
| 2 | 4 | 6 | 8 | 10 | 20 | 40 | 60 | 80 | 100 | 120
PARA | 0 | 0 | 0 | 0 | 0 | 0.030303 | 0.060606 | 0.11 | 0.27068 | 0.41212 | 0.525
MRLoc | 0 | 0 | 0 | 0 | 0 | 0 | 0.090909 | 0.17 | 0.34586 | 0.47273 | 0.575
PRoHIT | 0.66667 | 0.57143 | 0.8 | 0.69231 | 0.70588 | 0.57576 | 0.34848 | 0.28 | 0.22556 | 0.21818 | 0.205
Proposed | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
# of aggressor rows increases
Cannot mitigate RowHammer

## Slide 10
TWiCe [Lee+, ISCA’19], and Graphene [Park+, MICRO’20] cause significant hardware overhead to operate them
CBT [Sevedzadeh+, ISCA’18] carries out considerable additional refreshes to prevent RowHammer attacks
Previous Counter-based Methods
Chart: Relative # of Additional Refreshes
| 1.0011412108702045
TWiCe | 942.8
CBT | 64
Graphene | 53.8
Proposed | 23.2
Area overhead increases
Additional refreshes # increases

## Slide 11
Background
Existing Solutions
Motivation & Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 12
Motivation & Goal
Prior hardware-based methods have limitations, the methods:
  Cannot prevent complex RowHammer attacks
  Require tremendous area overhead
  Cause many additional refreshes (performance overhead)
Goal
  Provides protection against RowHammer even in the complicate attack patterns
  Operates with low area overhead and low # of additional refreshes

## Slide 13
Background
Existing Solutions
Motivation & Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 14
Key Idea & Overview of HammerFilter
Key Idea
  Each row has different degree of threat to cause RowHammer
  Track the level of threat of each row with modified Counting BloomFilter (CBF)
  Perform additional refreshes with a different probability according to the level
Overview
  HammerFilter decides the degree of threat based on access frequency
    Access frequency is tracked with basic operations of CBF (INSERT & COUNT)
  We introduce a new operation to CBF (HALF-DELETE) to reduce the level of threat of refreshed rows
    Refreshed rows have no risk of incurring RowHammer for a while
    + we can reduce unnecessary additional refreshes

## Slide 15
Why HALF-DELETE?
DELETE: subtracts each value in the hashed positions by COUNT value
  Impact on other accessed rows’ COUNT value
    - Hash-induced collision occurs
DELETE Operation

## Slide 16
Why HALF-DELETE?
HALF-DELETE: subtracts each value in the hashed positions by one-half of the COUNT value
  Avoid a hash-induced collision
HALF-DELETE Operation
COUNT{0x001b} = 4
COUNT{0xf323} = 1
COUNT{0x001b} = 4
COUNT{0xf323} = 1

## Slide 17
HammerFilter Implementation
CounterTable: stores access frequency of each rows
Hash Unit: hashes the row address to k bits; then, each bit is assigned to CounterTable’s indices
Insert Logic: updates aggressor row candidates with a certain probability
Delete Logic: reduces aggressor row candidate’s value when additional refresh is done
Count Logic: provides the extent of danger of accessed rows to the Refresh Logic

## Slide 18
HammerFilter’s Operation
    INSERT an accessed row to the CounterTable with a fixed probability, pi(0.005)
    Count Logic sends COUNT value to the Refresh Logic for every access
    Refresh Logic sends additional refresh commands to the victim rows with the probability according to a specific equation
    When additional refreshes are performed, Delete Logic performs HALF-DELETE

## Slide 19
Background
Existing Solutions
Motivation & Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 20
Experimental Methodology
Simulator
  DRAMSim2 (open-source DRAM simulator) integrated with gem5
Processor
  8 cores, 2 GHz, 8-wide issue, 7 MSHRs/core, OoO 192-entry instruction window
Last-Level Cache
  4 MB shared 64 B cacheline, 8-way associative
Memory Controller
  FR-FCFS, 54-entry request queue
Main Memory
  32 Gb device, x8 DDR4-3200, 1 channel, 1 rank, 16banks/rank, 64 K rows/bank, 1 KB page, 4K RH threshold

## Slide 21
Experimental Methodology
Workload
  19 benchmarks from SPEC CPU 2006 for benign applications
  Five pattern types of malicious attacks

## Slide 22
Background
Existing Solutions
Motivation & Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 23
Analysis in Malicious Applications
PARA-0.001, MRLoC, PRoHIT cannot reduce RowHammer sufficiently
HammerFilter achieves superior results
Chart: Aggressor Rows #
| 2 | 20 | 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 260 | 280 | 300 | 320
PARA-0.001 | 0 | 0.028902 | 0.1821 | 0.28112 | 0.43907 | 0.5037 | 0.57382 | 0.64371 | 0.67184 | 0.68616 | 0.70361 | 0.76604 | 0.71293 | 0.7541 | 0.75818 | 0.78302 | 0.70946
MRLoc | 0 | 0.028902 | 0.25 | 0.3133 | 0.47913 | 0.55704 | 0.59053 | 0.65083 | 0.71599 | 0.75656 | 0.78434 | 0.8 | 0.82177 | 0.82459 | 0.83273 | 0.89623 | 0.90878
PRoHIT | 0.76471 | 0.83237 | 0.75309 | 0.71674 | 0.65442 | 0.42074 | 0.23955 | 0.21259 | 0.18496 | 0.1969 | 0.20361 | 0.22893 | 0.27619 | 0.35574 | 0.42545 | 0.59198 | 0.91892
HammerFilter (Ours) | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Protect all

## Slide 24
Analysis in Benign Applications
HammerFilter performs a small number of additional refreshes
(1.5% of basic refreshes on average)
Chart: Relative # of Additional Refreshes
| bzip2 | h264ref | soplex | astar | milc | gromacs | omnetpp | perlbench | mcf | gobmk | hmmer | zeusmp | bwaves | sjeng | leslie3d | namd | sphinx3 | lbm | libquantum | average
PARA-0.001 | 1.0067 | 1.0008 | 1.0031 | 1.0068 | 1.0014 | 1.0019 | 1.0025 | 1.0032 | 1.0042 | 1.0062 | 1.0075 | 1.008 | 1.0073 | 1.0091 | 1.009 | 1.0002 | 1.0008 | 1.0092 | 1.0095 | 1.0051
MRLoc | 1.0073 | 1.001 | 1.0037 | 1.008 | 1.0015 | 1.0022 | 1.0034 | 1 | 1.0044 | 1.0065 | 1.0077 | 1.0086 | 1.0074 | 1.0091 | 1.0091 | 1.0003 | 1.0008 | 1.0092 | 1.0095 | 1.0052
TWiCe | 1.0012 | 1 | 1.0037 | 1.0042 | 1 | 1 | 1 | 1 | 1 | 1.0003 | 1.0124 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1.0011
Graphene | 1.0066 | 1 | 1.006 | 1.0065 | 1.0021 | 1.0011 | 1 | 1.0007 | 1 | 1.0073 | 1.0185 | 1.011 | 1.0005 | 1.0128 | 1.009 | 1 | 1 | 1.0117 | 1.0127 | 1.0056
PRoHIT | 1.0856 | 1.0192 | 1.0831 | 1.1168 | 1.0093 | 1.0429 | 1.1077 | 1.1188 | 1.1092 | 1.0881 | 1.1186 | 1.0981 | 1.0074 | 1.1127 | 1.1011 | 1.0089 | 1.0169 | 1.1142 | 1.1204 | 1.0778
CBT-4096 | 1.1925 | 1.021 | 1.096 | 1.2056 | 1.0416 | 1.0553 | 1.0763 | 1.0952 | 1.12 | 1.1886 | 1.2366 | 1.2255 | 1.1437 | 1.2693 | 1.2608 | 1.0077 | 1.0219 | 1.2686 | 1.2948 | 1.1485
HammerFilter (Ours) | 1.0233 | 1.0002 | 1.0114 | 1.0223 | 1.0006 | 1.0014 | 1.0006 | 1.0019 | 1.0023 | 1.0166 | 1.0311 | 1.0276 | 1.0271 | 1.0338 | 1.032 | 1 | 1.0001 | 1.0338 | 1.0327 | 1.0157
1.5%

## Slide 25
Area Overhead
HammeFilter requires smaller storage
  40.6 better than TWiCe
  2.3 better than Graphene
40.6
2.3

## Slide 26
Background
Existing Solutions
Motivation & Goal
HammerFilter
Experimental Methodology
Evaluation
Conclusion

## Slide 27
Conclusion
HammerFilter is a novel method to mitigate RowHammer
Provides robust protection for RowHammer attacks
Has negligible performance overhead
Operates with less area cost compared to previous counter-based methods